## Slide 1
SAIT DATA ANALYTICS CAPSTONE · 2026
Solar Energy Potential
Analysis Across Alberta
A Data-Driven Framework for the Alberta Utilities Commission
CWEEDS 1998–2017
SAIT Campus Solar 2018–2023
Python · scikit-learn
Power BI
Group 3 | Abiola Abosede Abioye, Prutha Chokshi, Samuel Chidubem Aduaka
Client: Alberta Utilities Commission (AUC)
Presented at the SAIT Capstone Showcase

## Slide 2
THE PROBLEM
What Gap Does the AUC Face Today?
!
Current State
Alberta holds some of Canada's strongest solar resources yet the AUC and municipalities base solar energy decisions on national averages, not the 20-year local climate records that already exist
Grid capacity planning
The AUC cannot accurately model distributed solar contributions without city-level yield predictions
Micro-generation policy
Setting fair interconnection rates requires knowing how much solar each Alberta cities generates
Municipal adoption targets
National-average data overstates potential in northern cities and understates it in southern ones
Developer guidance
Solar installers need location-specific tilt and sizing data the AUC cannot currently provide
✓
Our Solution
An end-to-end solar analytics pipeline delivering six outputs tailored to AUC planning needs:
D1
GHI Prediction Model
Random Forest R² = 0.917
D2
City Comparison Dashboard
Power BI for all 4 cities
D3
Panel Optimization Report
Tilt angles + payback tables
D4
Seasonal Heatmaps
Monthly GHI across 20 years
D5
Long-Term Trend Analysis
Mann-Kendall significance test
D6
SAIT Real-World Validation
Pattern correlation r = 0.97
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
1 / 11

## Slide 3
OUR APPROACH
Two Datasets · Four Cities · Six Deliverables
CWEEDS Dataset
Period
1998–2017 (20 years)
Records
701,280 hourly
Variables
GHI · DNI · DHI · Temp
Format
WY3 fixed-width
SAIT Campus Data
Period
Apr 2018 – Sep 2023
Records
13,423 quality hours
Systems
Carport + Rooftop PV
Use
Pattern validation
Four Alberta Cities — North to South
Edmonton
53.3°N
1,537 kWh/m²
Calgary
51.1°N
1,625 kWh/m²
Medicine Hat
50.0°N
1,659 kWh/m²
Lethbridge
49.7°N
1,688 kWh/m²
Annual POA yield shown; south-to-north latitude gradient drives the difference.
Analysis Pipeline
Clean
& Parse
→
Explore
& Feature Eng.
→
Train
ML Model
→
Optimize
Tilt & Payback
→
Trend
Analysis
→
SAIT
Validation
Why this matters
Unlike theoretical-only projects, we combine two datasets, one modelled weather record (CWEEDS) and one real measured generation feed (SAIT campus) validated against each other across a north-to-south city gradient
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
2 / 11

## Slide 4
DATA OVERVIEW
CWEEDS Variables and SAIT Campus Specifications
CWEEDS Key Variables and Analytical Role
Variable | Units | Role in Analysis
Global Horizontal Irradiance (GHI) | kJ/m² × 0.1 | Primary prediction target
Direct Normal Irradiance (DNI) | kJ/m² × 0.1 | Used for tilt angle optimization
Diffuse Horizontal Irradiance (DHI) | kJ/m² × 0.1 | Critical for cloudy-day modelling
Dry Bulb Temperature | °C × 0.1 | Panel efficiency derating (~0.4%/°C > 25°C)
Minutes of Sunshine | 0–60/hr. | Strongest ML feature - cloud-cover proxy
Dew Point Temperature | °C × 0.1 | Humidity / cloud formation proxy
Wind Speed | m/s × 0.1 | Panel cooling and soiling accumulation
Station Pressure | Pa × 10 | Air mass and surface irradiance
SAIT Campus Dataset
SOURCE
SAIT Great Hall Building (GBT)
PERIOD
Apr 8, 2018 – Sep 19, 2023
RESOLUTION
1-min intervals → resampled hourly
SYSTEMS
Carport Solar + Rooftop Solar
PEAK CARPORT
~15,391 Wh per reading
PEAK ROOFTOP
~7,199 Wh per reading
QUALITY RECORDS
13,423 hourly (complete hours only)
KNOWN GAP
2021 and 2022 sensor outages are excluded
OVERLAP W/ CWEEDS
None as CWEEDS ends 2017
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
3 / 11

## Slide 5
CITY COMPARISON
Annual Solar Yield — Lethbridge Leads; Edmonton Trails by 9.8%
Chart: 
| Edmonton | Calgary | Medicine Hat | Lethbridge
Annual POA (kWh/m²) | 1537 | 1625 | 1659 | 1688
1,688
kWh/m²/yr
Lethbridge
1,537
kWh/m²/yr
Edmonton
9.8%
Yield advantage
Lethbridge vs Edmonton
~1,200
Extra kWh/yr
per 10 kWp system
All four cities rank among the sunniest in Canada and even Edmonton outperforms most European solar markets
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
4 / 11

## Slide 6
SEASONAL PATTERNS
Monthly Solar Irradiance — 20-Year Climatology (1998–2017)
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Lethbridge
1,282
2,204
3,459
4,930
5,919
6,361
6,887
5,620
4,070
2,546
1,454
1,046
Medicine Hat
1,241
2,130
3,420
4,870
5,848
6,269
6,898
5,606
4,011
2,473
1,404
1,028
Calgary
1,199
2,130
3,374
4,758
5,712
5,954
6,394
5,268
3,817
2,397
1,366
966
Edmonton
966
1,841
3,146
4,601
5,763
5,973
6,104
5,115
3,537
2,064
1,108
754
Avg. daily total GHI (Wh/m²/day)
Low
High
What the pattern shows
July irradiance is 6–9× higher than December across all four cities a swing driven by day length, not latitude. Lethbridge and Medicine Hat hold the edge in nearly every month, while Edmonton's shorter winter days widen the seasonal gap the most
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
5 / 11

## Slide 7
MACHINE LEARNING
GHI Prediction Model — Random Forest R² = 0.917
0.917
Overall R²
(Random Forest)
36.6 Wh/m²
Mean Absolute
Error (MAE)
69.5 Wh/m²
Root Mean Sq.
Error (RMSE)
0.695
Baseline R²
(Linear Reg.)
City-Level R² on Held-Out Test Set
Chart: 
| Calgary | Edmonton | Medicine Hat | Lethbridge
R² | 0.905 | 0.917 | 0.922 | 0.922
Model Design & Key Features
TRAIN / VAL / TEST SPLIT
70% / 15% / 15% - chronological to prevent data leakage
STRONGEST FEATURES
sunshine_min, DNI, hour_sin/cos, clear_sky_index
WHY RANDOM FOREST
Captures nonlinear GHI–cloud interactions; handles zero-inflated night distribution
VS LINEAR REGRESSION
R² jumped 0.695 → 0.917; a 32% relative improvement
CROSS-CITY GENERALITY
Trained on all 4 cities jointly with one-hot encoding
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
6 / 11

## Slide 8
VALIDATION
SAIT Campus Validation — Real-World Pattern Consistency
r = 0.97
Pearson correlation
Normalized CWEEDS GHI vs SAIT measured PV generation
What this confirms
CWEEDS accurately represents the solar climate that real Calgary PV systems experience.
What Makes This Unique
Most comparable academic solar projects work entirely with historical weather data and produce theoretical estimates. We have real measured output from an operating Calgary PV system
Why No Direct Temporal Validation?
CWEEDS ends December 2017. SAIT data begins April 2018. There is no overlapping period for a direct time-matched comparison
What We Did Instead
A climatological consistency check: normalized historical Calgary GHI patterns (CWEEDS, averaged by month × hour) compared against the normalized SAIT PV generation profile (2019–2023) to test whether the seasonal and diurnal solar pattern captured by CWEEDS matches what the real system experiences
✓ The seasonal curve (summer peak, winter trough) matches almost perfectly between the two datasets
✓ The diurnal pattern (morning ramp, midday peak, afternoon decline) also aligns with near-zero offset
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
7 / 11

## Slide 9
OPTIMIZATION
Panel Tilt Angles and Payback Periods by City
Optimal Panel Tilt — Simulated 20°–60° Using POA Irradiance
40°
Lethbridge
Formula est.: 41°
39°
Medicine Hat
Formula est.: 41°
42°
Calgary
Formula est.: 42°
42°
Edmonton
Formula est.: 44°
Simple Payback Period — Base: $2.50/Wp · $0.14/kWh · PR = 0.80
City | 10 kWp Annual (kWh) | Best-Case | Base-Case | Worst-Case | 100 kWp Annual (kWh)
Lethbridge | 13,501 | 9.3 yr | 13.2 yr | 18.5 yr | 135,011
Medicine Hat | 13,274 | 9.4 yr | 13.5 yr | 18.8 yr | 132,744
Calgary | 12,999 | 9.6 yr | 13.7 yr | 19.2 yr | 129,993
Edmonton | 12,296 | 10.2 yr | 14.5 yr | 20.3 yr | 122,960
Best-case payback stays under 10 years in every city which is well within a 25-year panel lifespan
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
8 / 11

## Slide 10
TREND ANALYSIS
Long-Term GHI Trend — 1998–2017
Chart: Annual GHI (kWh/m²)
| 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Lethbridge | 1417.6 | 1364.3 | 1415.9 | 1429.3 | 1358.6 | 1383.7 | 1369.8 | 1379.4 | 1406.6 | 1386.2 | 1376.7 | 1416.5 | 1310.1 | 1372.9 | 1377.3 | 1403.7 | 1398.4 | 1443.4 | 1425 | 1489.6
Medicine Hat | 1415.5 | 1350.7 | 1393.4 | 1422.6 | 1329.3 | 1359.5 | 1360.9 | 1376.1 | 1378.9 | 1353.1 | 1357.2 | 1407.6 | 1304.2 | 1361.5 | 1361.2 | 1396.7 | 1372.8 | 1422.1 | 1388.9 | 1463.7
Calgary | 1337.9 | 1279.8 | 1353.2 | 1364.1 | 1295.3 | 1321.9 | 1270.8 | 1284.8 | 1316.5 | 1297.9 | 1305 | 1349.4 | 1243.2 | 1313.3 | 1294.5 | 1320.6 | 1351.8 | 1380.5 | 1341.2 | 1411.2
Edmonton | 1265.5 | 1222.5 | 1218 | 1263 | 1225.8 | 1248 | 1209.4 | 1227.4 | 1248.4 | 1221.5 | 1264.1 | 1275.9 | 1203.3 | 1251.8 | 1232.1 | 1264.6 | 1287.9 | 1322 | 1266.1 | 1278.6
Linear regression + Mann-Kendall test confirm direction and significance per city
City | Slope/decade | p-value | Significant?
Edmonton | +2.95 kWh/m² | 0.020 | YES ★
Calgary | +2.48 kWh/m² | 0.167 | No
Lethbridge | +2.17 kWh/m² | 0.196 | No
Medicine Hat | +1.56 kWh/m² | 0.340 | No
What This Means
Edmonton shows a statistically confirmed upward trend of +2.6 kWh/m²/decade - both linear regression and Mann-Kendall agree. The other three cities show positive but not-significant slopes: solar resources are stable, not declining
Investment implication
Stable resources = reliable expected yield for the AUC and investors to plan against
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
9 / 11

## Slide 11
CONCLUSIONS
Conclusions & Recommendations for the AUC
5 Key Findings
1
Lethbridge leads Alberta in solar potential
Annual POA 1,688 kWh/m² which is 9.8% more than Edmonton. Latitude is the primary driver
2
Random Forest model achieves R² = 0.917
All 4 cities exceeded R² = 0.90; CWEEDS data reliably predicts PV output hourly
3
SAIT pattern correlation: r = 0.97
Historical GHI and real campus PV profiles show near-perfect seasonal/diurnal alignment
4
Payback under 10 years achievable
Under optimistic assumptions, all four cities reach payback in under 10.2 years
5
Edmonton: only city with a significant GHI trend
+2.6 kWh/m²/decade (p = 0.02); the other three cities show stable resources
3 Recommendations to the AUC
1
Prioritize southern Alberta incentives
Lethbridge and Medicine Hat show 9.3–9.4-year best-case payback target these cities first for micro-generation programs.
2
Adopt city-specific tilt angles
Recommend 39° to 42° depending on city, not a provincial average, in installation guidelines
3
Commission a post-2017 CWEEDS update
Extend trend analysis with 2018 and present data to capture Alberta's recent renewable energy expansion
Total direct software cost: $0 · Methodology is fully open-source and replicable for any Alberta municipality
Solar Energy Potential Analysis Across Alberta | SAIT Data Analytics Capstone 2026 | Group 3
10 / 11

## Slide 12
Acknowledgement
Group 3 | SAIT Data Analytics Capstone 2026 | Client: Alberta Utilities Commission
SAIT’s Applied Research and Innovation Services’ (ARIS) - Green Building Technology Access Centre (GBTAC)

## Slide 13
Thank You
Questions & Discussion
References
• Environment and Climate Change Canada. (2023). Canadian Weather Energy and Engineering Datasets (CWEEDS)
• Natural Resources Canada. (2023). Canadian Weather Year for Energy Calculation (CWEC). Open Government Portal
• Duffie, J. A., & Beckman, W. A. (2013). Solar Engineering of Thermal Processes (4th ed.). Wiley
• Gadiwan, A., & Shahbazi, M. (2019). Rooftop solar energy potential of Calgary. University of Calgary
• Chen, T., & Guestrin, C. (2016). XGBoost: A scalable tree boosting system. ACM SIGKDD
• Alberta Utilities Commission. (2024). Micro-generation regulation. auc.ab.ca
Group 3 | SAIT Data Analytics Capstone 2026 | Client: Alberta Utilities Commission